## Slide 1: Institute for Flow Physics and Control
Thomas Corke
Director, Institute for Flow Physics and Control
University of Notre Dame
College of Engineering
Notre Dame, IN
tcorke@nd.edu
University of Notre Dame

## Slide 2
Institute for Flow Physics and Control
SIGNATURE RESEARCH AREAS
PARTICIPANTS
20 T&R Faculty
8 R Faculty
12 Technical Staff
75 Ph.D. Students (85% U.S. citizens)
11 U.S. Govt. Agencies
25 Companies
Aero-acoustics
Aero-optics
Fluid-structure Interactions
Gas-turbine Propulsion
Hessert Laboratory
White Field Laboratory
Wind Energy
Multi-phase Flows
Plasma Dynamics
Sensors and Flow Control Actuators
Hypersonic Aerodynamics

## Slide 3
Low-Speed Wind Tunnels
Initial investigations utilizing flow visualization and other flow diagnostic tools (hot-wire, LDV, PIV, etc)

## Slide 4: Component Facilities
Army/Honeywell/UND VAATE Program
40Bar Blow-down Facility
In-draft Tri-Sonic Facility

## Slide 5: Anechoic Wind Tunnel
Sound Pressure Level (dB)
Sample Beam Forming

## Slide 6: Experimental Facilities Vision
Actual Applications
Government and Industry
Testing Facilities
Power
Typical
University
Envelope of
Highest Relevance
Technology Readiness
FlowPAC Target Capability

## Slide 7: Mach 0.6 Wind Tunnel
3’x3’x9’ test sections
Large optical access
Low turbulence
Temperature controlled
1750 H.P. motor
Variable R.P.M. AC
8’ diam., 2-stage fan
1000 ton-hr ice-storage chilled water cooling

## Slide 8: Helicopter Dynamic Stall Facility
Focused Schlieren Images

## Slide 9: Airframe Noise
Gulfstream 550 Nose LG

## Slide 10: Transonic Compressor Facility
400 H.P.
15,000 R.P.M.
Design tip-Mach: 1.2
Magnetic levitation rotor bearings
Rotor optical access

## Slide 11: Transonic Turbine Facility: LPT & HPT Modules
800 H.P. compressor
500 H.P. motor
Design 300 H.P. turbine
Magnetic levitation rotor bearings
Highly-loading rotor design
HPT
LPT

## Slide 12: Hot Annular Nozzle Cascade (HANC)
700°F primary flow
Transonic nozzle Mach numbers
Full secondary cooling systems
46 inch diameter
Controlled inlet turbulence characteristics.
Highly detailed aero/thermal measurements

## Slide 13: Front Stage Core Compressor (FSCC)
800 H.P.
Variable IGV
Transonic tip Mach number
Magnetic levitation rotor bearings

## Slide 14: Arc Heated Hypersonic Wind Tunnel
10m3 Internal Volume
500kW Maximum Power
Mach Nos. 3, 4.5, 6 & 9
Max. T0 = 4200K
Run Time ~ 1s
Minimizing test gas contamination: pure nitrogen arc-heating to prevent plasma induced chemical reactions in air, e.g., NOx production in plasma
Time Resolved Unstart Flame Dynamics
Freestream Flow

## Slide 15
Notre Dame - AFRL/AFOSR Collaboration+
Non-intrusive Flow Property Measurements for Supersonic/Hypersonic Flows
(2012/2013 Air Force Summer Faculty Fellowship Program)
Wright Patterson Air Force Base
(Dr. Campbell D. Carter)
Turbulent combustion enables hypersonic flights: turbulence property quantification & investigation of flame dynamics in supersonic/hypersonic flows.
Optically resolved unsteady ethylene flame dynamics at Mach 4.5, 6 and 9 scramjet flight conditions.
A short-gated (35 ns measurement time) laser diagnostics method for fuel concentration/gas density measurement in high-speed unsteady reacting flows is proposed and tested.
The new method will be used in RC-19 supersonic wind tunnel at Wright-Patterson Air Force Base to measure fuel concentration/temperature field in a scramjet combustor
Instantaneous Plasma
Emission Spectra near Flame Zone
Locations of Plasma Probe in a Reacting Flow
*H. Do and C. D. Carter (2013) Combustion and Flame 160: 601–609
Experimental Investigation of Turbulent Flames in Hypersonic Flows
(AFOSR Grant, FA9550-12-1-0161)
Air Force Office of Scientific Research
(Dr. Chiping Li & Dr. Campbell D. Carter)
*Do & Carter (2013)
X-51A, Waverider
+Hyungrok Do, PI

## Slide 16: Refractive-Index-Matched (RIM) Flow Facilities*
Large-scale RIM
Small-scale RIM
NaI Storage units
Processor
2 Closed-loop flow tunnels
NaI processing system
Piping system
Storage
Temperature controlled
Pressure resistant (N2)
Corrosion resistant
Scratch resistant
Sediment recirculation (ϕ = 2 mm)
N2
Laboratory overview
Total volume: 4200 liters
Velocity up to ~ 2 ms-1
Cross section: 0.45 m x 0.45 m
Length: 2.5 m
Large-scale RIM
Permeable boundaries
Bluff Bodies
Complex 3D topography
Applications
*AFOSR MURI, Ken Christensen PI

## Slide 17: Supersonic Mixing Facility
Mixing Enhancement and Flame Stabilization in High-Speed Combustion Systems by Transient Plasma*
*Proposal by Sergey Leonov.
In review, Chiping Li (AFOSR)

## Slide 18: Wind Energy Laboratory (eWiND)
25kW Turbines:
30’ Diameter
59’ Hub Height
Pitch Controlled
Meteorological Tower:
3-component, fast response ultrasonic anemometers
Temperature
Humidity
Pressure

## Slide 19: Airborne Aero-optics Laboratory
Dynamic correction of optical distortions produced by compressible flow structures
Falcon 10

## Slide 20: FlowPAC Fabrication Shop
Num. Lathe
5 Axis Mill
4 Axis Mill

## Slide 21: High Fidelity CFD
HPT Tip Clearance Analysis
Embedded Large Eddy Simulation (ELES)
(375M Mesh Points, 512 Processor Cores)

## Slide 22
AIAA J., 50, 1, 123-130 (2012); AIAA J., 51, 3, 657-664 (2013)
The free electrons, neutrals, metastables, and ions in an ionized gas can affect the permittivity to EM waves.
Change in the permittivity affects refractive index >>> Plasma Adaptive Optics (PAO). Technology Driver: Bandwidth
Plasma optics OPD depends on the length of the plasma, electron density, EM wavelength, gas composition, and heavy particle density.
Plasma Adaptive Optics
DARPA DSO: Brian Holloway
Metamaterials are designed with a lattice structure of materials having two indices of refraction.
Conventional metamaterials are designed for a single EM wavelength.
Lattice tuning capability with a broad range of positive and negative plasma permittivity offers numerous applications.
Tunable Plasma Metamaterials
AFOSR MURI: Mitat Birkan
60GHz
Patent: 8513583
PAO
PAO Array

## Slide 23: Plasma Temperature/Pressure Sensor
Pulse-detonation Engine
Temperature Mode
Pressure Mode
Patents: US7275013B1, US7908115

## Slide 24: Boundary Layer Transition Control
40%
NASA Mach 3.5 0.5m Quiet Nozzle
4° AoA 14° Cone Model
d=76μm
d/λ=0.43
λ
d

## Slide 25: AFOSR Proposal in AF Academy Mach 6 Facility*
0.5m
0.98m
Same size test section, will accommodate existing model.
Provides same Rex range as previous NASA experiment.
Intended to examine effect of higher Mach number and “noisy” environment on transition control.
*In review: Rengasamy (Pon) Ponnappan

## Slide 26
Hypersonic High-Reynolds-Number Quiet Tunnel
15min. Range at Mach 6 & 9
Advanced Hypersonic Weapon (AHW-2):
  Army, Navy
Tactical Boost Glide:
  Air Force, Navy, DARPA
Hypersonic Air-breathing Weapon Concept (HAWC)
  AFRL High Speed Strike Weapon (HSSW)
Glide: Boeing, Raytheon, Lockheed Martin
Air-breathing: Boeing, Raytheon
$180M CRAD for technology maturation
DoD Hypersonic Vehicle Programs
Motivation
China reported to have had 3 hypersonic boost-glide flights in 2014.
Schmisseur AIAA-2013-2606

## Slide 27
Hypersonic High-Reynolds-Number Quiet Tunnel
Key issue is on the accurate prediction of if and where turbulent transition occurs.
Determines the degree of heat transfer to the vehicle.
Motivation
Kimmel, “HIFiRE-1 Hypersonic Flight Test”, 2012
noisy
quiet
2x
Rex-trans (x106)
40
?
Flight Rex-trans
Ground tests require hypersonic wind tunnels that can simulate flight conditions:
  Low disturbances
  Natural transition Reynolds numbers
3x

## Slide 28
High Reynolds Number Mach 6 & 10 Quiet Wind Tunnel
Present “quiet” hypersonic wind tunnels are limited in quiet zone length, LQ
  TA&M Blow-down: ReLQ=6M
  Purdue 9” Ludwieg Tube: ReLQ=13M
Natural transition in these facilities only observed when instability growth is accelerated by geometry or disturbance generators.
Ludwieg tubes with large diameter, long, slow expansion axisymmetric nozzles that suppress cross-flow and Görtler instabilities.
Throat suction and heating to suppress TS.
STATUS QUO
LQ
SOLUTION
UND DESIGN
Mach 6 & 10 quiet zone to Rex≥40M.
33’ long nozzle, 2’ I.D. test section.
200’ long, 2.5’ I.D. driver tube.
80,000 gal. vacuum tank.
2 sec. run time.
1 hr. run frequency.
P0 ≤ 10Bar > acceptable throat waviness ~1-2 mil./in. (NC lathe).
Throat heated to ~670K (~750°F) to minimize TS growth.
Notes: Include notes that would be helpful to the reader or someone (other than yourself) who needs to understand the details. Ideally the chart will be useful even without the author to explain the details. Also include references to published papers plus URLs to online versions if available.
Keep in mind that somewhere or other in this chart, each of these questions should be answered:
1. What technical challenge is being undertaken on behalf of the project
2. Why is it hard and what are the open problems
3. How has this problem been addressed in the past
4. What new intellectual tools are being brought to bear on the problem
5. What is the main intermediate achievement
6. How and when does this achievement align with the project roadmap (end-of-phase or end-of-project goal)
7. What are the even long-term objectives and consequences?

## Slide 29
High Reynolds Number Mach 6 & 10 Quiet Wind Tunnel
200 ft. (61 m)
Building expansion (nozzle, test section, and diffuser plus labs and office space
Existing White Field Laboratory (subsonic tunnel, turbomachinery test cells, etc.)

## Slide 30: Vital Statistics
Tunnel configuration | Ludwieg tube | 
Mach number | 6.0 | 
Nozzle exit diameter | 0.60 m | 24 in.
Nozzle length | 10 m (!) | 33 ft.
Throat diameter | 0.084 m | 3.3 in.
Stagnation pressure (quiet flow) | 1 MPa, 10 atm | 150 psia
Stagnation temperature | 430 K | 310 ºF
Freestream unit Re (quiet flow) | 11*10^6 /m | 3.4*10^6 /ft.
Re_L (based on quiet-flow core length) | 40*10^6 | 
Free jet test section length | 0.9 m | 3 ft.
Driver diameter | 0.74 m ID | 30 in. OD
Driver length | 61 m | 200 ft.
Vacuum capacity | 300 m^3 | 80,000 gal
Run time | 2 s | 
Run frequency | Pending compressor & pumps, ~ 1 /hr | 
Re variation during run | -9% | 

## Slide 31: Mach 6 Performance Estimates

## Slide 32
Boeing has committed FY15 funds to CFD design of Mach 6 nozzle.
Pending DURIP submitted to ONR/AFOSR).
Seeking other corporate support.
Seeking UND benefaction support.
Estimated $3.1M Phase I.
Mach 6 operation 24 mo. from funding start.
Engineering design and major fabrication at UND.
Phase II Mach 10 design starting in Year 3 from start of funding.
SCHEDULE
High Reynolds Number Mach 6 & 10 Quiet Wind Tunnel

## Slide 33: Mach 6&10 Quiet Tunnel Size Perspective